Schematics, drawings, etc.

---
Robot schematics
DC Motor 30 rpm
Current sensor
Current sensor
Charging plates
Bluetooth
OUT
OUT
TX
RX
Arduino MEGA
Current sensor
Current sensor
Motor driver
TX
OUT
A5
RX
OUT
ENB
IN4
Mower motor
IN3
A4
IN2
Battery
IN1
D2
A3
ENA
D3
A2
+12V
+12V
A1
Voltage
D5
A0
GND
D6
Inductor
D11
D10
D9
Audio amplifier
DC Motor 30 rpm
Current sensor
OUT
GND
OUT
IN

---
Base station schematics
Bluetooth
Charging plates
Perimeter wire, 12V, 25ohm, ~0.5A, 6W
TX
Current sensor
RX
OUT
Arduino Pro Mini
Current sensor
Perimeter wire driver
OUT
ENB
IN4
IN3
IN2
IN1
ENA
RX
TX
A1
A0
12V charger
D6
D7
+12V
D8
GND

---
Connectivity
Serial over bluetooth
<
Base station
PC
Serial
Robot
Smartphone

---
Controller smartphone app
Romeo
SELECT
START

---
Bluetooth Configuration Setup
HC-05
RXD Voltage divider
FTDI-232

---
HC-05 module
BUTTON

---
Logo
Romeo
Romeo

---
Robot – top & left view
50 mm
Electronics
300 mm
Battery 12V
300 mm

---
Base station – top & left view
400 mm
150 mm
70 mm

---
Current sensor
+5V
VIN, 0-1V
Measure current through Rs.
+
VOUT, 0-5V
LM384
-
Rs
D0
GND
VOUT = VIN * (1 + R3 / R2)
D0: 1N4148
Rs: 0.1 ohm, 1W
R2: 10k ohm
R3: 39k ohm
R3
R2
GND